# The Vamp Audio Analysis Plugin API: A Programmer's Guide
written and deftly illustrated by Chris Cannam
Overview
A Vamp plugin is a chunk of compiled program code that carries out analysis of a digital audio signal, returning results in some form other than an audio signal. These results are often called audio features.
Vamp plugins are distributed in shared library files with extension .dll, .so, or .dylib depending on the platform, with one or more plugins in each library. A plugin is usually identified to the computer using the shared library name plus a short text identifier naming the plugin within the library. The plugin cannot be used on its own, but only with a conforming “host” application which loads the plugin from its shared library and calls functions within the plugin code to configure it, supply it with data and run it.

Plugins are not supplied with the whole of their audio input at once, but instead are fed it as a series of short blocks: in this respect they resemble real-time audio processing plugins, but in all other respects they are executed “off-line”, meaning that they are not expected to run in real-time and are not obliged to return features as they occur.
The Vamp plugin binary interface is defined in C, and the plugin SDK (software development kit) which will be described here is written in C++. Plugin authors are recommended to use the C++ interfaces in preference to plain C.
Vamp is not an acronym. It contains letters suggestive of audio, plugins, visualisation and so on, but not in the right order.
#### Examples
Throughout this document we will use as examples three types of feature extractor that already exist as Vamp plugins. We will not consider the serious audio processing necessary to implement these techniques; we only describe how they communicate with the host as plugins. They are:
- Note onset detector. This estimates the times at which new note events begin in the signal, and returns those times as results. There are no particular values associated with the times.
- Chromagram. This example of a visualisation data extractor analyses audio and produces from it a grid of values, with a time step as the X coordinate and a pitch bin within the octave as the Y coordinate. Each value in the grid describes the “strength” of the corresponding pitch in the music within the given time range.
- Amplitude tracker. This calculates structurally simple two-dimensional data (time and value) from the audio, to be displayed by the host as a data plot or used for some other purpose.
As these examples show, Vamp plugins do not actually do any display or user interaction: they just return data. In most cases, these data are not the final result of the work the host is doing, but are useful for something else – either for a host to display and the user to interact with in some way, or as intermediate calculations for a particular purpose such as semantically meaningful audio editing. Vamp plugins do not do swirly visualisation and are not very useful in real-time contexts such as interacting with musical performers.
What does a Plugin Contain?
A Vamp plugin needs to make a certain amount of information available to the host.
Every plugin, no matter how simple, should provide the following:
1. The identifier, name, and description of the plugin itself.
   See “Identifiers, Names and Descriptions” below.
2. The name of the maker of the plugin, and the plugin's copyright status and version number.
3. The input domain which the plugin would like its audio provided in.
   See “Inputs” below.
4. The plugin's preferred step size and block size for audio input.
   See “Step and Block Size” below.
5. The minimum and maximum number of input audio channels the plugin is capable of handling.
6. A list of Output Descriptors that contain information about the structure of the results that the plugin may produce.
   See “Outputs” below.
7. Implementations of standard functions that set up, reset, and run the plugin. (*** NB: no section heading on this rather crucial subject yet!) The C++ base class provides virtual methods to override for these.
Some plugins have parameters that can be set to adjust the way they do their processing. These plugins will also need to provide:
1. A list of Parameter Descriptors that contain information about the editable parameters of the plugin. The host may use these descriptors to show the user a control window for the plugin, for example.
   See “Parameters” below.
2. Implementations of standard functions that retrieve and set the values of parameters. The C++ base class provides virtual methods to override for these.
A plugin may also have a set of pre-defined configurations that can be offered to the user by name. These are known as programs and a plugin that supports them will also need to provide:
1. A list of program names.
   See “Programs” below.
2. Implementations of standard functions that retrieve the current program name and select a new one. The C++ base class provides virtual methods to override for these.
Base classes

Identifiers, Names and Descriptions

### Categories
Inputs
The inputs to a Vamp plugin are audio data, with one or more channels. The plugin can specify how many channels it will accept using its getMinChannelCount and getMaxChannelCount methods.
To supply audio data and run the plugin, the host calls the plugin's process method repeatedly. Each time process is called, it is passed a single “block” of audio of a known size in samples. The block size is fixed when the plugin is initialised, and must be the same for all subsequent calls to process.
The audio may be provided in either time domain or frequency domain form. Time domain audio input is conventional PCM sampled digital audio with a floating-point sample type; frequency domain input is the result of applying a windowed short-time Fourier transform to each input block. The input domain is specified by the plugin using its getInputDomain method.
Besides the block size, there is also a “step size” which is the difference in sample count between the input to one process call and the next. This is most often relevant when using frequency domain input, as the next sections should make clear.
### Time Domain
When a plugin requests time domain input, the host divides the audio input stream up into a series of blocks of equal size, and feeds one to each successive call to process. The process call may then return features derived from that audio input block, according to its whim.
When all of the audio data has been supplied, the host calls getRemainingFeatures, and the plugin returns any features that are now known and not yet been returned from earlier process calls.

It is most usual with time domain input for the step size to be equal to the block size, as shown above. This means that the plugin is receiving every sample in the audio input exactly once, in a series of contiguous blocks of data.
This does not have to be the case – the plugin can return a different value for getPreferredStepSize to that returned from getPreferredBlockSize if for any reason it would prefer to receive overlapping or non-contiguous blocks. This is very often the preferred mode of operation when using frequency domain input.
### Frequency Domain

Outputs
### Feature Structure

### Sample Types and Timestamps
Every feature that is returned from a Vamp plugin has a time associated with it. This is the time at which the feature is considered to “start”, as a fractional number of seconds since the start of the audio input.
The time may be explicit – stored in the timestamp of the feature structure itself – or implicit – omitted from the feature itself and instead deduced by the host on the basis of the sample type and rate defined for the output in which the feature is returned. Whether the time is implicit or explicit depends on the sampleType field of the output and the hasTimestamp field of the feature.
The permitted sampleType values for an output are:
- OneSamplePerStep – Implicit time: the effective time of any feature returned by process for that output is the same as the time that was passed in to the process function by the host. The host should not read the timestamp from the output feature, even if the feature's hasTimestamp field is true.
- FixedSampleRate – Implicit time: the effective time of the first feature returned by the first call to process for that output is the same as the time that was passed in to the process function, and the effective times of any subsequent features from this or all remaining process calls increment according to the sampleRate specified in the output descriptor. Again, the host should not read the timestamp even if it is present.
- VariableSampleRate – Explicit time: the time of each feature is returned in the timestamp of the feature, and the feature's hasTimestamp field must be set to true. The feature may have a “resolution” given by the sampleRate value for that output, but the host may ignore it.
You may notice that the hasTimestamp field in the feature structure is actually redundant. There is no situation in which the host will use hasTimestamp to decide whether to read the timestamp or not. If the sample type is VariableSampleRate, the host must always read and use the timestamp; if the sample type is anything else, the host will never read the timestamp.

Configuration
### Parameters
### Programs
### What Can Depend on a Parameter?
One difference between Vamp plugins and most real-time audio processing plugin APIs is that the Vamp plugin may need to make significant aspects of its operation – such as the preferred input step and block size – dependent on the parameters used to configure it.
For this reason, a Vamp plugin must be completely configured by the host, with its parameters and programs set, before it is initialised; the parameters cannot be changed afterwards. Furthermore, some properties of the plugin can depend on the values passed in to the initialise function, so the host must query these again after initialisation but before calling process.
The properties that a plugin may decide to change on the basis of its parameter and program settings are:
1. Its preferred input step size and block size.
2. Everything within the Output Descriptor for any output – the number of values per output (binCount), sample type and rate, extents and so on – except for the identifier, name, and description fields of the output. Also, the plugin may not change its total number of outputs.
Everything listed in (2.) above may also change depending on the number of channels, step size, and block size passed in to the initialise function.
Host Extension
### Loader
### Adapters
Appendix I: Contents of a Plugin Library
Appendix II: An Annotated Example Plugin

[Fri Jan 25 2008] [15:08:30] <las>	cannam: where i am right now is that a "Feature" is a particular point in time (possibly); it may or may not have a set of values associated with it
[Fri Jan 25 2008] [15:08:40] <cannam>	basically you get a set of feature outputs, and each of those consists of a sequence of feature vectors, either regularly spaced or at variable intervals... you're right, it's not obvious is it?
[Fri Jan 25 2008] [15:08:52] <cannam>	las: that's about right
[Fri Jan 25 2008] [15:09:05] <cannam>	las: a Feature always has a time, and may have zero or more values
[Fri Jan 25 2008] [15:09:33] <las>	cannam: the mental problem for me was that i was imagining that the plugin might return multiple different kinds of info, and that "Feature" referred to a specific kind of info
[Fri Jan 25 2008] [15:09:40] <cannam>	las: you can get more of an idea for a specific plugin by running it in vamp-simple-host and looking at how it prints the results
[Fri Jan 25 2008] [15:09:43] <las>	cannam: i.e. "Feature 3 occurs at a, b, c and d"
[Fri Jan 25 2008] [15:10:02] <las>	cannam: as opposed to "there is a feature at a, b, c and d"
[Fri Jan 25 2008] [15:10:07] <cannam>	las: that would usually be an "output", i.e. "output 3 has features at a, b, c and d"
[Fri Jan 25 2008] [15:10:24] <las>	cannam: is they all have times, what is hasTimestamp for?
[Fri Jan 25 2008] [15:10:40] <cannam>	or, "this output has features at a, b, c and d with value X and features at e and f with value Y"
[Fri Jan 25 2008] [15:11:40] <cannam>	las: the "sample type" of the output specifies whether the features are equally spaced (in which case the timestamps are implicit), or will have individual timestamps
[Fri Jan 25 2008] [15:12:12] <cannam>	las: so you only set, and read, the timestamps if the sample type is something other than "one sample per step"
[Fri Jan 25 2008] [15:12:37] <cannam>	las: however, this aspect of vamp "isn't well thought out"
[Fri Jan 25 2008] [15:13:18] <cannam>	las: in that the timestamp is either mandatory (if the sample type is not one sample per step), or else it should be totally ignored (if the sample type is one sample per step)
[Fri Jan 25 2008] [15:13:52] <cannam>	las: there is no situation in which the host ever actually needs to take notice of hasTimestamp, although I suppose it can check it and warn if it's false for a sample type in which the timestamp is needed
[Fri Jan 25 2008] [15:14:26] <cannam>	las: that may be revised in a future vamp release, but not until we have other things worth breaking the api for as well -- no hurry there
[Fri Jan 25 2008] [15:15:05] <las>	cannam: this is where your "functional package" idea comes in
[Fri Jan 25 2008] [15:15:36] <las>	cannam: since i am not writing a generic "load this VAMP plugin and run it" host, but rather using VAMP to do specific work, i wasn't inspecting the OutputList of PercussionOnset
[Fri Jan 25 2008] [15:16:55] <las>	cannam: ergo, something that just took audio and gave me back results would be handy (but not essential). i don't know how many other uses of VAMP might be similar.
[Fri Jan 25 2008] [15:17:09] <cannam>	las: probably quite a few
[Fri Jan 25 2008] [15:17:26] <cannam>	las: that's definitely the way I was thinking
[Fri Jan 25 2008] [15:22:28] <las>	cannam: now i am totally confused. looking at the code for the perc onset process() call, it appears that it generates either zero or 1 onset per process call
[Fri Jan 25 2008] [15:23:10] <cannam>	las: never attempt to read the top sekrit code
[Fri Jan 25 2008] [15:23:28] <cannam>	las: but yes, that's exactly what it does
[Fri Jan 25 2008] [15:23:59] <cannam>	las: its "resolution" therefore is limited to the step size, which is 512 samples
[Fri Jan 25 2008] [15:36:05] <las>	cannam: ok, thats actually entirely reasonable :)
[Fri Jan 25 2008] [15:36:36] <cannam>	las: the resolution could be much better; making a higher resolution version particularly for tracks that are expected to contain nothing much besides percussion is on my todo list
[Fri Jan 25 2008] [15:38:01] <las>	cannam: isn't that a 15 min task?
[Fri Jan 25 2008] [15:38:34] <cannam>	las: well, tuning these things is actually rather fiddly
[Fri Jan 25 2008] [15:38:53] <cannam>	las: you can make an instant "higher resolution version" by using a much smaller step size, but you won't necessarily get better results out of it
[Fri Jan 25 2008] [15:39:13] <las>	cannam: oh my, that explains why this is kind of slow too. stepsize = 512, blocksize = 1024; its reading all the data twice :(
[Fri Jan 25 2008] [15:39:37] <las>	cannam: maybe i should update the vendor branch with that buffering adapater stuff
[Fri Jan 25 2008] [15:39:48] <cannam>	las: that would certainly avoid that problem
[Fri Jan 25 2008] [15:39:57] <cannam>	las: though it would still be fft'ing all the data twice
[Fri Jan 25 2008] [15:40:46] <las>	cannam: hmm
[Fri Jan 25 2008] [15:41:05] <las>	cannam: so this where i should do my own FFT and pass it spectral data?
[Fri Jan 25 2008] [15:41:08] <cannam>	las: with this sort of stuff, 10% of the work is deciding on a method, 90% is tuning it -- that's why it's worth making plugins of these things & reusing the code even though the real work may be only a few lines
[Fri Jan 25 2008] [15:41:34] <cannam>	las: unfortunately, with this method you do actually want it to do the fft twice
[Fri Jan 25 2008] [15:41:44] <las>	cannam: really?
[Fri Jan 25 2008] [15:41:47] <cannam>	las: it's an overlapped shaped window
[Fri Jan 25 2008] [15:41:51] <las>	cannam: ok
[Fri Jan 25 2008] [15:41:58] <las>	cannam: yes, i remember reading that
[Fri Jan 25 2008] [15:42:33] <cannam>	las: if you don't use a shaped window, you get a lot of noise in the fft resulting from the "edges" of your window being treated as part of the (theoretically infinite) signal
[Fri Jan 25 2008] [15:42:52] <cannam>	las: and if you do use a shaped window, you have to have an overlap or you miss some material
[Fri Jan 25 2008] [15:43:03] <las>	cannam: ok, i'll update the vendor branch from svn now
[Fri Jan 25 2008] [15:44:12] <cannam>	las: let me know if it works!